ALIGNMENT

WHAT IS IT?
Memory is organized in cells:

Each cell has a certain amount of bits it can store. When you define a variable one or more cells are used by the program:

When the CPU operates on that varaible it needs to move it into its register.
A CPU can use a CLOCK to read a WORD from the memory.
The problem arises when we have a variable that is (because of some offset) stored in two variables:
(assuming word = 16 bits)

That means that x occupies half of the first cell, and y occupies the remaining of the first cell AND half of the second cell.
Let's say we wanted to read y. The CPU would need 2 clocks to access the data because it will use one clock to find the data in 0x00 and another clock for the data in 0x01.
However, we can align y and use padding to shift it all to the second cell:

Luckily for us, this is done automatically by the compiler to avoid misalignment.
This will also introduce an alignment requirement to every structure, which is that of the largest member of the struct.

However, the automatic padding brings us to a new issue.
Let's say we have the following struct:

In theory, the size of this struct should be 7. However, when we use sizeof(X) we discover it is 12 (~42% increase!). This is because of the alignment requirement.
Because our alignment requirement is 4, our struct actually looks like this:

This leads to a lot of wasted space. However, if we reoganize our struct to be like this:

Here we have taken into account the alignment requirement and minimized the amount of padding
the compiler creates for us.
Expected size: 7
Padded size: 8

In the last two examples we can see that the compiler adds padding at the end of the struct, seemingly unnecessarily. However, lets say that we have an array of our structs:

Assuming the base address of x is 0x00. If X occupies 7 bytes, the second array element will be at 0x00 + 0x07 = 0x07. Meaning that the int variable of our struct will be at 0x07, which is not a multiple of 4 and therefore conflicts with the alignment requirements of int. Leading to the issue we discussed at the beginning.
The best way to avoid padding is to put the variables in a struct in decreasing size.

NOTES:
std::alignment_of<T> can be used to get the alignment requirement of the type.

std::alignas can be used to set the alignment of a variable.

Uses of alignas: https://stackoverflow.com/questions/45478824/c-alignment-when-to-use-alignas#:~:text=Use%201%20%2D%20Avoiding%20unnecessary%20invalidation,cache%20line%20of%20another%20core.

std::align
Given a pointer to a buffer of a certain size, returns a pointer aligned by the specified alignment for a size equal to the number of bytes and decreases the space argument by the number of bytes used for alignment. The first aligned address is returned. The function modifies the pointer only if it would be possible to fit the wanted number of bytes aligned by the given alignment into the buffer. If the buffer is too small, the function does nothing and returns nullptr.
Extremely useful for memory manager (!!!)

BIT FIELDS